Rivestimento pareti in laminato ABET inciso con macchina CNC

Il rivestimento della parete che costeggia la scala che conduce al piano interrato è caratterizzato da pannelli rifiniti in laminato plastico, sul quale è stato inciso un motivo decorativo di bicchieri e bottiglie variamente orientati inteso ad enfatizzare il prodotto merceologico qui dominante, ossia il vino.

Questa decorazione è stata realizzato mediante l’incisione con macchina CNC del layer superiore di un rivestimento a due strati (uno bianco ed uno nero) di laminato plastico ABET dello spessore di 3+3mm applicato alle pannellature delle pareti. L’asportazione dello strato superficiale inciso (bianco) ha messo in luce lo strato inferiore (nero), dando così luogo ad una finitura parietale con effetto di bassorilievo, estremamente durevole e – data la natura del materiale impiegato - facile da pulire.

Il manufatto è stato realizzato in Italia dall’azienda

IFAS Tasselli

di Roberto Tasselli

Industria arredamenti

Strada Nazionale della Cisa, Km.163

SUZZARA  46029 (Mantova)

Italia

Ph.: 0039.0376.532051

Fax: 0039.0376.511293

tasselli@ifas.it

www.ifas.it

e poi messo in opera in situ

____________________________________________________________

The cladding of the wall located along the stairs leading to the basement features a decorative pattern of variously oriented bottles and glasses, which highlights the predominantly sold product in this shop, i.e. wine.

Such pattern was obtained by engraving with a CNC machine a double layer (a white and a black one) of 3+3mm thick opaque ABET laminated plastic glued onto the wall panelling.

Once peeled off, the white layer has unveiled the black one underneath, giving life, this way, to a “bas-relief” wall covering, extremely lasting and easy to clean.

Such work has been carried out in Italy by the company

IFAS Tasselli

di Roberto Tasselli

Industria arredamenti

Strada Nazionale della Cisa, Km.163

SUZZARA  46029 (Mantova)

Italia

Ph.: 0039.0376.532051

Fax: 0039.0376.511293

tasselli@ifas.it

www.ifas.it

and successively laid on the walls “in situ”