Doha Tower

Proposal

Operating Management

HBS

Trading & Contracting Co.

DOHA Tower

Offices

Owner

H.E. Sheikh: Saud Bin Mohamed Bin Ali Al-Thani

The Best Tall Building in Middle East & Africa 2012

Council on Tall Buildings and Urban Habitat Chicago – USA

DOHA Tower Offices

A)  Introduction:

The Doha Tower Offices, located on the Corniche road in the centre of Doha City, is a landmark addition to the prominent features of Doha city where it occupies interface and is overlooking the waters of the Gulf.  The development is situated only a few metres away from the Ministries and Government Departments and 15 minutes from Doha International Airport.

The Tower is cylindrical in shape and measures 45meters in diameter. It is capped by a dome and topped by a lightning conductor at a level of 231.5meters above groundwith a total built up area of approximately 110,000 square meters.

The Tower has been designed by innovative French Architect Messrs Atelier Jean Nouvel. The design is unique and it is the first design of a Tower with reinforced concrete dia-grid columns in a cross (X)shape covered at the external facade by geometric complexity of the oriental moucharabiahand butterflies in the shape of Bee’s heaves acting as a sun screen. The inner layer is aluminum curtain walling with slightly reflective glass that protect from the sun’s rays. There is a walkway between the sunscreen and the curtain walling that allow for maintenance to wash and clean the curtain wall.

Each floor offers panoramic views towards the Cornice Road and the Gulf to the East and South, the downtown of Doha City to the West with the Peal Qatar and Lusailon view Town to the North.

In addition to itsdistinguished location and shape, the Tower has been finished with quality material and equipmentthat is incompliance with the highest International Standards. The Tower is equipped with the latest fire fighting systems that match the criteria adopted in the State (NFPA) governing the design of such systems and the latest security systems, surveillance cameras and access control system programmed to control entry of individuals into the court yards and each floor of the Tower. In addition is the availability of a passenger control system that distributes the passengers among the lifts with a sophisticated system for the movement of the elevators.

B)  Advantage of the Tower:

Tenant of the Tower will enjoy the following unique advantage:

- All offices are with a net height of 3meters. The floors are comprised of galvanized raised flooring that facilitates the electrical connections and other services.

- High flexibility in the distribution and division of offices.

- False ceiling equipped with lighting, smoke detectors and sprinklers as part of the fire fighting system. In addition all tower areas are covered with an affective fire alarm system complete with a voice system in case of evacuation.

- Pantry / buffet room equipped with the necessary apparatus.

- Toilets for men and women on each floor in addition to a separate toilet for the disabled.

- High-tech air conditioning system.

- An advanced Building Management System (BMS).

- The latest communication systems and the internet through a network of Fiber Optic cables for telephone and high speed internet network services that serve both Q- Tel and Vodafone. In addition, each floor is equipped with a communication rack and Data/Telephone outlets covering the whole floor area.

- A comprehensive satellite TV system.

- Restaurant at Level 42 with panoramic views of Doha City and the Corniche

- A programmed system for external lighting with LED lightingwhich highlights the Tower in a stunning form at night.

- All levels contain two exit doors, water outlet, hydraulic Lift and walkway between the sun screen and the curtain walling to facilitate the cleaning and maintenance of the curtain walling. In addition the walkways could be open to access from the outside of the Tower, to the upper and lower levels for cleaning purposes and in the event of emergency situations.

- Fire exit and fire escape methods using special lifts only operate during fire accidents, being implemented in accordance with the Civil Defense Department and International Specifications.

- A landscaped green area in a unique design cover more than 40% of the land area and contains a vertical garden which is the first of its kind in the State of Qatar.

- Easy access to the Tower. In addition to the availability of car parking areas that accommodate 900 cars for the Offices.

C) The Main Components of the Doha Tower:

DohaTower is consists of 49 floors devoted tooffice and car parking at the Basement floors distributed as follows:

- Public Lobby comprises of reception area,  offices,  and rooms for supervision and security on the ground floor with a total area of 1500 M²,

- Offices at Mezzanine level with a total area of 680 M²

- 41 floors of offices with a total built up area of 42,132 M². The area of floors is ranging between 1071 M² and 922 M² with an average of 1053 M²

- Restaurant at level 42with a total area of 576 M² and a capacity of 80 customers.

- Offices for VIP at level 43 with a total area of 730 M²

- Offices for VVIP at level 44 with a total area of 954 M²

- Special gate for the VIP at level -7 M

- Public Services at each level comprised of the following:

  - Toilets for Male (3 Nos)

  - Toilets for Female (2Nos)

  - Toilets for the disabled at each floor

  - Plant rooms for electricity and other services

  - Public toilets  at the Basement floors

- Offices for security services at level -7 M with atotal area of 57 M²

- Offices for Safety services at level -7 M with atotal area of 31 M²

- Offices for technical supervision at level -7 M with a total area of 28 M²

- Separate building of two floors for  electricity stations and cooling services

- Three Basement floors for the car parking that accommodate 870 cars for the Offices only. The car parking area is equipped with fire alarm withautomatic sprinkler system that functions in the case of fire. Each Basement floor includes two escape routes that are fire and smoke resistant in addition to huge fans that extract the smoke from the fire affected floors and air pressurizes the upper and lower levels to prevent smoke transfer to unaffected areas to ensure safe evacuation of occupants from the building.

- Fire fighting room at level (-4m) with a total area of 57 M².

- Area for loading and off loading goods in the north side of Basement 1.

- Water storage tanks for public use and for firefighting purposes.

- Stores (closed)  for storage purposes at the Basement levels with a total area of 4604 M²

D)  Lifts

The estimation of the number of the lifts and the speed of the same has been achieved following specialized study that adopted the highest International Standards and modern techniques. The control of the lifts movement is based on a modern technique that control and guide the user (Destination Control System). On the basis of this modern Destination Control System the Tower was provided with 23 elevators for multiple uses as shown below:

- 8 Panoramic lifts (glass) with a speed of 6meters/second for public use travelling up to level 27.

- 4 High Rise Lifts  with a speed of 8meters/second serve all levels up to level 41

- One Lift with a speed of 8meters/second for VIP

- One special Lift  for VVIP with a speed of 0.13 meter/second for service between levels 42, 43 and 44

- 2 Lifts for fire fighting with a speed of 4 meters/second travelling up to level 42.

- 2 Lifts with a speed of 2.5 meters/second for Public Services travelling up to level  42

- 4 Lifts with a speed of 0.75meter/secondserving the three Basement levels (Car Parking) up to the lobby.

- One Lift with a speed of 0.5 meter/second for loading located in a separate building for the electricity stations and cooling serves the three basement levels.

It is to be recorded that the maximum waiting time for the Lift is not exceeding 20 seconds which resulted from the implementation of the Destination Control System.

E) Service and PowerStationBuilding

The Service Buildingconsists of two floors. The ground floor has been a located for the electrical Sub-Station which contains the high tension switchgear (11 KV), 10 No power transformers (1250 KW each), and low tension switchgear which feeding all the systems and utilities in the Tower. The first floorhas been allocated for the chillerequipment for the air conditioning and all the auxiliary equipment that feed it.

F) Specialized Security and Communication Systems

The Tower has been provided / equipped with the latest high tech communication system and fiber opticcables for telephone and high speed internet services, with specialized security systems to control the entry of individuals and their movement at each entrance and egress to the floors. The Tower has been equipped also with an advanced closed circuit television monitoring system (CCTV) which will allow the security personnel to follow the movement of the visitors and staff within the Tower.

The Tower is also equipped with a very advanced access control system controlling all the entrance and egress to the towerthrough gates and barriers as well as controlling vehicle access to the basement floors. The barriers are linked with direct communication / contact with the security personnel in emergency conditions. Each of these systems have been linked to a comprehensive and effective Building Management System (BMS) which could detect any failure / or malfunctions that may occur on any of the aforementioned systems through screens showing all details and information needed to assist theoperation and maintenance team of the Tower.

G) Mechanical Systems

The Tower has been equipped with its own central cooling system using chilled water from nine chillers which ensure moderate temperature around the clock.This has been done through two Air Handling Units (AHUs) on each floor handling the cold air and achieving a low level of noise resulting from the operation of machinery systems by using sound attenuators on the air supply and return attached to these two units. The fresh air supply is provided to floors by main fresh air handling units available at the mechanical rooms that provide the building with fresh air supply after being treated and cooled.

H) Fire Alarm and Fire Fighting Systems

All Tower areas are covered with an effective fire alarm system together with voice system in case of evacuation with specialized links to the lifts, doors, fans, gates, barriers,.etc, to make the way clear in case of evacuation.

The Tower is served by an automatic sprinklerssystem that is sensitive to flames and functions during the event of fire. Each floor includes two escape routes that are fire and smoke resistant. The Tower has been equipped with huge fans that extract the smoke from the fire affected areas and pressurizes air to the upper and lower levels to prevent smoke transfer to unaffectedareas to ensure safe evacuation of the occupants from the building while the smoke is discharged to outside the building.

(I) And also the Tenant of the Tower will enjoy the following unique advantage:

- The Tower is fully insured by Commercial Bank Of Qatar.

- The Tower has Cleaning Dept. Contains 35 Cleaners for cleaning the tower by Daily basis.

- The Tower has Maintenance Dept. Contains 25 persons (Maintenance Manager, Mechanical Manager, Electrical Manager, and Supervisors & Technicians.

- The Tower has Security Dept. Contains 25 persons for 24 hours

- The Tenant has the right to access & using the elevators, parking’s, etc.. For 24 hours per day, seven days per week at no extra cost.

- The Tenant has the right to reserve one parking for every 50 sq meters, in addition, sufficient for the visitors in the public parking.

(P) Office Areas to be used for each Level in the Tower

| Level | Description | Purpose | Total Area M² |
| --- | --- | --- | --- |
| 00 | Ground level | Public Lobby | 527 |
| 0 | Mezzanine level | Offices | 680 |
| 1 | 01st level | Offices | 1071 |
| 2 | 02nd level | Offices | 1061 |
| 3 | 03rd level | Offices | 1058 |
| 4 | 04th level | Offices | 1046 |
| 5 | 05th level | Offices | 1077 |
| 6 | 06th level | Offices | 1063 |
| 7 | 07th level | Offices | 1055 |
| 8 | 08th level | Offices | 1050 |
| 9 | 09th level | Offices | 1063 |
| 10 | 10th level | Offices | 1043 |
| 11 | 11th level | Offices | 1041 |
| 12 | 12th level | Offices | 1037 |
| 13 | 13th level | Offices | 1045 |
| 14 | 14th level | Offices | 1024 |
| 15 | 15th level | Offices | 1017 |
| 16 | 16th level | Offices | 1013 |
| 17 | 17th level | Offices | 1022 |
| 18 | 18th level | Offices | 1002 |
| 19 | 19th level | Offices | 996 |
| 20 | 20th level | Offices | 984 |
| 21 | 21st level | Offices | 996 |
| 22 | 22nd level | Offices | 997 |
| 23 | 23rd level | Offices | 982 |
| 24 | 24th level | Offices | 973 |
| 25 | 25th level | Offices | 982 |
| 26 | 26th level | Offices | 967 |
| 27 | 27th level | Offices/Transfer | 922 |
| 28 | 28th level | Offices | 1000 |
| 29 | 29th level | Offices | 963 |
| 30 | 30th level | Offices | 1148 |
| 31 | 31st level | Offices | 1140 |
| 32 | 32nd level | Offices | 1119 |
| 33 | 33rd level | Offices | 1110 |
| 34 | 34th level | Offices | 1088 |
| 35 | 35th level | Offices | 1067 |
| 36 | 36th level | Offices | 1055 |
| 37 | 37th level | Offices | 1047 |
| 38 | 38th level | Offices | 1012 |
| 39 | 39th level | Offices | 976 |
| 40 | 40th level | Offices | 938 |
| 41 | 41st level | Offices | 883 |
| 42 | 42nd level | Restaurant | 576 |
| 43 | 43rd level | VVIP Offices | 730 |
| 44 | 44th level | VVIP Offices | 954 |