AW - Red Rock House

Located in a small Berkshires township on a densely wooded, 16-acre property, this site afforded no views and little sun penetration, its topography defined by a steep slope, a vertical rock ledge, and a creek prone to seasonal flooding.

The project embraces a “machine in the garden” design approach, where contemporary vocabulary and minimal form underscore the relationship between built work and natural landscape. The initial design strategy focused on manipulating the site to preserve as much of its natural topography as possible. A 200-foot long board-formed concrete retaining wall runs north—south along the site’s east edge, exposing new plateaus for buildings, garden, and meadow. Clinging to this wall, the guesthouse anchors the building assembly in the steep hillside, while the main house and deck project out from the landform into the treetops. A linear bluestone path connects guesthouse and main house, and leads to the west balcony in the treetops, looking out over the creek below.

A minimal materials palette evokes both rusticity and precision, reflecting the juxtaposed orders of landscape and architecture. Buildings are clad in a high performance rainscreen of knotty western red cedar, milled with multiple profiles to generate a pattern that changes with the sun’s movement. The boards are organized within vertical bays delineated by aluminum T-sections, producing a textured rhythm that accommodates openings, fenestration, and screens. Lattice volumes created with aluminum L-sections indicate primary entrance and screen interior spaces from southern exposure. Interiors are entirely white, emphasizing the play of light, the client’s collection of art, and views of the landscape.

Credits

Name of project: Red Rock House

Location: Red Rock, New York

Completion Date: September 2013

Gross square footage: 6400 sf (includes both main house and guest house/garage)

Architect:

Anmahian Winton Architects

650 Cambridge Street

Cambridge, MA 02141

(617) 577-7400

# Architect Project Team:

Nick Winton, AIA (Principal in Charge) and Alex Anmahian, AIA (Consulting Principal)

Makoto Abe, Project Architect

Sydney Thiel, LEED AP and Mazen Sakr, Design Team

Engineers:

Structural Engineer:

RSE Associates, Inc.

Richmond So, Sofya Auren

63 Pleasant Street, Suite 200, Watertown, MA 02472

(617) 926-9300

Civil Engineer:

Morris Associates P.L.L.C.

9 Elks Lane, Poughkeepsie, NY 12601

(845) 454-3411

Consultants:

Landscape:

Reed Hilderbrand LLC Landscape Architecture

Douglas Reed, John Kett, EB Randall

130 Bishop Allen Drive, Cambridge, MA 02139

(617) 923-2422

General Contractor:

Lou Boxer Builder, Inc.

1 Day Farm Road, West Stockbridge, MA 01266

(413) 232-7116

Photographer:

Jane Messinger

(857) 928-8213

General Specifications

Structural System

Concrete foundation with steel frame with metal deck concrete floor, wood frame with TJI joists

## Exterior Rainscreen Cladding

Wood:  Red Cedar siding with Penofin Verde stain

Metal: Rheinzink Zinc tiles, Custom Aluminum profile and screen

Moisture Barrier: #30 Asphalt Saturated Felt

## Roofing

Sarnafil PVC

## Windows

Wood frame: Duratherm Window Corporation, Marvin Windows and Doors

## Glazing

Glass: PPG

Skylights: Velux

## Doors

Wood doors: Duratherm Window Corporation

Sliding doors: Duratherm Window Corporation

## Hardware

Locksets: GU

Pulls: FSB

## Interior Finishes

Cabinetwork and custom woodwork: Amherst Wood Working

Floor and wall tile: Bluestone, Quartered White Oak

## Lighting

Interior ambient lighting: Color Kinetics, io Lighting, Artemide

Downlights: Engineered Lighting Products, Lightolier, RSA, Tech Lighting

Exterior: BK Lighting, Custom

## Plumbing

Duravit, Dornbracht