## Slide 1
Code 1200

## Slide 2
INTRODUCTION
The intent of this design was to work within the context of the Indian cultural narrative with a new language of interpretation that allows for a dynamic, varied and yet enduring experience for the end user.
The spine of the design is the exuberant use of colors, which is a key element of the Indian culture. The subtle yet definitive use of colors to connect with the space without being overwhelming and out of sync presented a new challenge. The mainstay of the theory is the large volume that starts right from the entrance spanning till the lobby for individual rooms. The design intent for it was achieved by having all the surfaces connected to this volume in a single tone of color blue .This move creates an illusion of a chunk of mass being subtracted and separated from the overall volume. Keeping the spaces muted around this scoop further ensures that there is emphasis on this space being the mainstay of design.
Another example of an inspired use of color is how the color black is used in this space. Black, which is typically considered taboo, if used wisely can offer a new interpretation of other colours and elements around it. In this project, the colour black provides a contrast and context to the other colours.
We have attempted to continue the Indian cultural narrative by using local raw materials. The textures of these individual raw elements, such as brick and stone were highlighted using available natural light. The material palate consists of Godhra brick tiles, concrete floor and stained Birch plywood in its raw form. At the same time there are elements like colored PU, back painted glass and matte black paint that balance out the rusticity.
The intent has been to provide an ‘experience’ to the end user that is unpredictable and dynamic. Creating such an experience surely involves risk-taking for the designers, but the reward is an unprecedented yet a enduring experience for the clients.

## Slide 3
Walls demolished
EXISTING LAYOUT

## Slide 4
PROPOSED LAYOUT

## Slide 5
ARTWORK & SCULPTURES

## Slide 6
A
B’
B
SECTIONS
C’
C
D
D’

## Slide 7
Section B-B’ Through Lounge, Dining and living area
A
A’
B’
B
Section A-A’ Through Living area, The scoop, Master bedroom

## Slide 8
C’
Section C-C’ Through Master bedroom and Daughters bedroom
C
D
D’
Section D-D’ Through Entrance and foyer, Dining area, Balcony

## Slide 9
ENTRANCE

## Slide 10
Gypsum ceiling
3mm corten sheet
Name laser cut
3mm corten sheet
ELEVATION
SECTION
Entrance:
Entrance of the apartment sets the tone for the a modern yet an Indian contemporary design. The Rustic corten steel panel at the entrance is beautifully accentuated by the light falling on it from the top. The entrance is adorned with a rustic seating and Exclusive artefacts which make the entry to the house grand yet bespoke. The raw nature of the rusted corten steel is brought to notice by the wall washer light that grazes the surface of the panel. Right next to this panel sits a bench designed in post modern era. Laser cut backlit suspended letters form the name plate within the corten steel panel.
DECOR
Grazer light
ENTRANCE SOFA
12mm plaster +pop
Brick wall
Ply backing
3mm corten sheet
Ply backing
3mm corten sheet
Ply backing
3mm corten sheet
12mm plaster +pop
12mm plaster +pop
DETAILS
Foam Seat + Artificial leather
Birch plywood
25mm dia pipe in black powder coating

## Slide 11
Entrance

## Slide 12
ENTRANCE FOYER

## Slide 13
Entrance Foyer:
The entrance lobby is part of the central theme of the house, ‘The Blue Scoop’. The entire volume here is rendered in a single tone of blue color. The idea behind that is to create an illusion of a small chunk of the volume being subtracted from a larger volume that constitutes the overall apartment. The relief here comes in the form of an artwork created using the creative use of jute by known artist Manish Nai.
Artwork & lighting
Entrance console :Elevation
Entrance console :Plan
Slatted MDF sheet 12 x12mm finished in grey PU
19mm ply finished in 4mm veneer finished in grey PU
19mm ply finished in 4mm veneer finished in grey PU
Slatted MDF sheet
12 x12mm finished in grey PU
Detail B
12mm back painted
Slatted MDF sheet
12 x12mm finished in grey PU
Slatted MDF sheet
12 x12mm finished in grey PU
19mm ply finished in 4mm veneer finished in grey PU
19mm ply finished in 4mm veneer finished in grey PU
Detail A
RCC slab
Necessary ply support
Ply backing finished in 4mm veneer finished in back paint
AC Vent
Ply backing finished in 4mm veneer finished in back paint
AC Vent detail
A
B

## Slide 14
Entrance Foyer:

## Slide 15
Entrance foyer through living area

## Slide 16
LIVING ROOM

## Slide 17
Living room:
The Living space is flanked by the Blue scoop that gets separated by a razor-sharp line. The palette of this space consists of Godhra Bricks, oak wood slatted ceiling, stained birch plywood, concrete slurry floor, and a certain amount of Matt black wall surfaces. There is a deliberate attempt to make the lights part of the slatted profile of the ceiling in a way that hides them from plain sight. There is an ample amount of light that enters from the west side filtering through the balcony overhang. The setup is of a contemporary European furniture offsetted by antique Indian Artefacts. Large hand knotted rug binds the loose furniture around it seamlessly.
Elevation
Side table detail
RCC slab
Curtain pelmet
Grazer light
Ply framework
Wooden slats
Brick cladding
Brick cladding
2mm Aluminium plate
Brick wall
TV console
Ardex flooring on marble base
6mm thk plate finished in matt black powder coating
8mm dia rod finished in matt black powder coating
Brick wall detail
Antiques and sculptures

## Slide 18
Living Room

## Slide 19
Living Room

## Slide 20
LOUNGE AND BAR COUNTER

## Slide 21
Lounge and bar counter:
The original use of this space was a bedroom with an attached toilet which was accessed from the temple area. During the planning stage, it was connected from the living side and the transitional space was turned into a linear bar. To deem the mood of space casual and relaxed the bricks on the wall were teamed up with busy patterned sofa low in height. The artwork chosen here is also of ruins of vintage cars that add to the rusticity of space.
RCC slab
12mm Ply pelmet
Grazer light
Wooden Slats
Brick cladding
Brick wall
Stone cladding
RCC slab
Ardex flooring on marble
Aluminium skirting
Stone cladding
Elevation
Brick wall detail : Ceiling
Brick wall detail : Skirting
Artworks in contrast with the wall

## Slide 22
BAR COUNTER
Lounge area
Bar from dining area

## Slide 23
MASTER BEDROOM

## Slide 24
Master Bedroom:
Being in line with the color theory, you are drawn into space by a long row of reflective red glass shuttered wardrobe. Again the opening of the space being on the western side, there is harsh sunlight entering the space. To counter that, the hue of the room was kept neutral in nature. The highlighter wall is done in the local stone cladding that holds the balance of the room. The choice of art here is a contemporary 3D collage that changes in viewpoint while one moves through the space ensuring that each time it’s a unique experience.
RCC slab
Aluminium skirting
TV console
Stone cladding
Aluminium Patti screwed to the door
Handle grip
4mm back painted glass
4mm back painted glass
Light weight door made in aluminium box section framing with 6mm ply on both sides
Elevation
Stone wall detail
Door shutter detail
Antiques and lighting.

## Slide 25
drawer
drawer
fixed
Wash basin
Plywood top with 4mm thk polished veneer
Shelf made of metal sheet cladding on framing finished in black powder coating
Metal framework
Elevation
Elevation
Plan
Master Bathroom:
This long space is a combination of walk-in closet and master toilet. The mood of the volume is set to dark. Wardrobes are custom made in black tinted glass, the floor is local Basalt and the ceiling is slatted oak wood. The use of mirrors on the short and long sides in strategic locations achieves infinite reflectivity.
Elevation

## Slide 26
Master bedroom

## Slide 27
Master bedroom

## Slide 28
DAUGHTER’S ROOM

## Slide 29
Daughters Bedroom:
Here, you are brought into the space flanked by a long row of wardrobe on one side in a shade of pink back painted glass and mirrored shutters on the other. The space is divided into two parts by use of a stepped-up wrap around volume made up of stained birch plywood around the bed and the adjoining study on one side. The other side of the space is made of the concrete floor with the ceiling height wardrobes. The arrangement of the room is minimal by choice to emphasize the volumetric moves.
Stone cladding
Ardex flooring on marble subfloor
Aluminium Skirting
Ply backing
Birch ply
Polished plywood table top
8mm dia solid rod finished in black powdercoating
Raised platform detail
Plan-Metal framework
Plan
Elevation A
Elevation B
Elevation

## Slide 30
Daughters bedroom

## Slide 31
Daughters bedroom

## Slide 32
GUEST BEDROOM

## Slide 33
Guest Bedroom:
This is a fairly small space compared to the others. Being consistent with the other spaces the mood of this room was set to be dark. The walls and the wardrobes go into the greyscale while the bed head-board wall breaks the monotony by use of bricks in part.
Elevation
Brick wall
Ply backing
Veneer finished
in black paint
Grazer light
Brick wall cladding
RCC Slab
Ply pelmet
Grazer light
Curtains
Sliding window
Aluminium plate
Ply Backing
Plaster finished in paint
Aluminium skirting
Detail A
A
Lamp
Side table

## Slide 34
Guest bedroom

## Slide 35
Guest bedroom